## Slide 1: Section 13 (week of Dec 4): Computer Architecture, part 1
We'll start at 5:01 (Tuesday) and 7:16 (Wednesday) Eastern Time. 1
  Pset 5 was due at start of the lecture 13 week at 9am. Pset 6 and Term project are due at start of the final exam week at 9am. 2 See the Notes.
  Important Dates
  Your questions
  Binary Arithmetic
  Signed Integers In Binary
  Octal and Hexadecimal Numbers
  MIPS Architecture
  MIPS Sample code
1 Zip file with this section’s slides and sample code is posted to course’s page
2 Last late submission window closes on Wednesday, Dec 20 at 9am

## Slide 2: Important Dates
Nov 13 | Submit term project proposals Submit pset 4
Dec 4 | Submit pset 5
Dec 11 | Practice final posted
Dec 17 | Practice final review
Dec 18 | Submit pset 6 Submit term project
Dec 20 | Pset 6 late submission window closes at 9:00 AM Term project late submission window closes at 9:00 AM
Dec 20-21 | Final exam window
Jan 4 | Grades available at Online Services https://extension.harvard.edu/login/

## Slide 3: Binary Arithmetic
0 + 0 = 0 0 + 1 = 1 1 + 0 = 1 1 + 1 = 0, carry the 1
1 1 1 310 = 0 0 0 0 0 0 1 1 710 = 0 0 0 0 0 1 1 1 + 210 = 0 0 0 0 0 0 1 0 + 610 = 0 0 0 0 0 1 1 0 --- --------------- ---- --------------- 510 = 0 0 0 0 0 1 0 1 1310 = 1 1 0 1

## Slide 4: Binary Arithmetic
0 + 0 = 0 0 + 1 = 1 1 + 0 = 1 1 + 1 = 0, carry the 1
1 1 1 310 = 0 0 0 0 0 0 1 1 710 = 0 0 0 0 0 1 1 1 + 210 = 0 0 0 0 0 0 1 0 + 610 = 0 0 0 0 0 1 1 0 --- --------------- ---- --------------- 510 = 0 0 0 0 0 1 0 1 1310 = 1 1 0 1

## Slide 5: Signed Integers In Binary
8 bits can represent 28 = 256 numbers = -128 thru 127 = -27 thru 27-1
n bits can represent 2n numbers = -2n-1 thru 2n-1-1
To negate a number, take its "two's complement"
  Complement (~) and increment (cia )

## Slide 6: Signed Integers In Binary
8 bits can represent 28 = 256 numbers = -128 thru 127 = -27 thru 27-1
n bits can represent 2n numbers = -2n-1 thru 2n-1-1
To negate a number, take its "two's complement"
  Complement (~) and increment (cia )
610 = 0 0 0 0 0 1 1 0

## Slide 7: Signed Integers In Binary
8 bits can represent 28 = 256 numbers = -128 thru 127 = -27 thru 27-1
n bits can represent 2n numbers = -2n-1 thru 2n-1-1
To negate a number, take its "two's complement"
  Complement (~) and increment (cia )
610 = 0 0 0 0 0 1 1 0 ~610 = 1 1 1 1 1 0 0 1

## Slide 8: Signed Integers In Binary
8 bits can represent 28 = 256 numbers = -128 thru 127 = -27 thru 27-1
n bits can represent 2n numbers = -2n-1 thru 2n-1-1
To negate a number, take its "two's complement"
  Complement (~) and increment (cia )
610 = 0 0 0 0 0 1 1 0 ~610 = 1 1 1 1 1 0 0 1 1 + ~610 = 1 1 1 1 1 0 1 0 = -610

## Slide 9: Signed Integers In Binary
8 bits can represent 28 = 256 numbers = -128 thru 127 = -27 thru 27-1
n bits can represent 2n numbers = -2n-1 thru 2n-1-1
To negate a number, take its "two's complement"
  Complement (~) and increment (cia )
610 = 0 0 0 0 0 1 1 0 ~610 = 1 1 1 1 1 0 0 1 1 + ~610 = 1 1 1 1 1 0 1 0 = -610 710 = 0 0 0 0 0 1 1 1 = 710 -- ---------------

## Slide 10: Signed Integers In Binary
8 bits can represent 28 = 256 numbers = -128 thru 127 = -27 thru 27-1
n bits can represent 2n numbers = -2n-1 thru 2n-1-1
To negate a number, take its "two's complement"
  Complement (~) and increment (cia )
610 = 0 0 0 0 0 1 1 0 ~610 = 1 1 1 1 1 0 0 1 1 + ~610 = 1 1 1 1 1 0 1 0 = -610 710 = 0 0 0 0 0 1 1 1 = 710 -- --------------- = 0 0 0 0 0 0 0 1 = 110

## Slide 11: Challenge: Signed Integers
What does 1 1 1 1 1 1 1 1 represent?
Sign-bit == 1 implies it's a negative number
To see its positive value, cia it.
    ~ 1 1 1 1 1 1 1 1 = 0 0 0 0 0 0 0 0
    + 1 --------------- 0 0 0 0 0 0 0 1
So 1 1 1 1 1 1 1 1 represents -1.

## Slide 12: Challenge: Signed Integers (continued)
What does 1 0 0 0 0 0 0 0 represent?
Sign-bit == 1 implies it's a negative number
To see its positive value, cia it.
    ~ 1 0 0 0 0 0 0 0 = 0 1 1 1 1 1 1 1
    + 1 --------------- 1 0 0 0 0 0 0 0
So 1 0 0 0 0 0 0 0 represents a negative number that can't be negated.
So 1 0 0 0 0 0 0 0 represents -12810

## Slide 13: Octal and Hexadecimal Numbers
Octal and hexadecimal are useful because their digits are 3 or 4 bits.
0xFF = FF16 = 1 1 1 1 1 1 1 12 = -110 ------- ------- 0377 = 3778 = 1 1 1 1 1 1 1 12 = -110 --- ----- -----

## Slide 14: MIPS Architecture
MIPS data sizes:
MIPS memory is byte-addressable
  half word's byte address must be divisible by 2
  word's byte address must be divisible by 4
MIPS has 32-bit general-purpose registers named r0 thru r31.
  $t0 thru $t9: “temporary registers” (by convention subroutines might change them).
  $s0 thru $s7: “saved registers” (by convention subroutines won't change them).
  $a0 thru $a3: argument registers.
  $v0 thru $v1: return value registers.
  …
 |  | 1 byte | 8 bits
 | 1 half-word | 2 bytes | 16 bits
1 word | 2 half-words | 4 bytes | 32 bits
See “Useful MIPS Links & Documents” on the course’s page
See HelloWorld.asm

## Slide 15: MIPS Architecture
MIPS is a “load/store” architecture
  Load data from memory into registers, do a computation, store result in memory
    lw, lh, lb, la sw, sh, sb
  Can use “immediate operands” stored directly in instructions
    li $t0, 99 addi $t0, 12 addi $t0, -12 # there is no subi instruction
  Indirect addressing
    la $t0, table loop: lw $t1, ($t0) … addiu $t0, 4
    b loop
  Move data between registers
    move $t2, $t1 # $t2 contains value in $t1

## Slide 16: MIPS Architecture
Branch and jump instructions
  b ## b someLabel # branch unconditionally
  beq, beqz ## beqz $a0, someLabel # branch if $a0 = 0
  bne, bnez ## bne $t0, $t1, someLabel # branch if $t0 ≠ $t1
  blt, bltz, bltu ## blt $t0, $t1, someLabel # branch if $t0 < $t1
  ble, blez, bleu
  bgt, bgtz, bgtu ## Use unsigned comparisons with memory addresses
  bge, bgez, bgeu ## since memory addresses can’t be negative.
  branch destination is a 16-bit (±2**15) word offset from current location
  j someLabel ## jump unconditionally to someLabel
  jump destination is 23-bit offset

## Slide 17: Strategy for writing MIPS programs
Step 1: Solve the problem in Java Step 2: Translate your Java into MIPS
Java:
MIPS:
if ( $t0 <= 0 ) { ... // $t0 <= zero } else { ... // $t0 > zero }
if ( !($t0 > 0) ) { ... // $t0 <= zero } else { ... // $t0 > zero }
if: bgt $t0, $zero, else ... # $t0 <= zero b done else: ... # $t0 > zero done:
See for1.asm, for2.asm, for3.asm, if_then_else.asm, while.asm, process_a_table.asm

## Slide 18: MIPS Sample Code: Syscalls & Assembler Directives
Directive | Meaning
.data | The next items are data to be put in the user data segment.
.text | The next items are instructions to be put in the user text segment.
.ascii "string" | Store the string in memory, but do not null-terminate it.
.asciiz "string" | Store the string in memory and null-terminate it.
.byte b1, ..., bn | Store the n 8-bit quantities in successive bytes of memory.
.half h1, ..., hn | Store the n 16-bit quantities in successive halfwords of memory.
.word w1, ..., wn | Store the n 32-bit quantities in successive words of memory.
Action | Syscall Code in $v0 | Arguments | Result
print int value | 1 | $a0 = integer value | Value is printed
print string | 4 | $a0 = string address | String is printed
read int value | 5 |  | $v0 = int value
read string | 8 | $a0 = buffer address, $a1 = max length | String is read
exit | 10 |  | Program exits